## Slide 1
Segurança Informática
CTeSP Tecnologias e Programação de Sistemas de Informação
Filipe André Martins de Freitas

## Slide 2: Firewall Technologies
Upon completion of this section, you should be able to:
Explain how firewalls are used to help secure networks.
Describe the various types of firewalls.
Configure a classic firewall.
Explain design considerations for implementing firewall technologies.

## Slide 3: Securing Networks with Firewalls

## Slide 4: Defining Firewalls
All firewalls:
Are resistant to attack
Are the only transit point between networks because all traffic flows through the firewall
Enforce the access control policy
Notes: 4.2.1.1 Defining Firewalls

## Slide 5: Benefits and Limitations of Firewalls
Notes: 4.2.1.2 Benefits and Limitations of Firewalls

## Slide 6: Types of Firewalls

## Slide 7: Firewall Type Descriptions
Packet Filtering Firewall
Stateful Firewall
Application Gateway Firewall
NAT Firewall
Notes: 4.2.2.1 Firewall Type Descriptions

## Slide 8: Packet Filtering Firewall Benefits & Limitations
Notes: 4.2.2.2 Packet Filtering Firewall Benefits and Limitations

## Slide 9: Stateful Firewalls
State Tables
Stateful Firewalls
Stateful Firewall Operation
Notes: 4.2.2.3 Stateful Firewalls

## Slide 10: Stateful Firewall Benefits and Limitations
Next Generation Firewalls
Granular identification, visibility, and control of behaviors within applications
Restricting web and web application use based on the reputation of the site
Proactive protection against Internet threats
Enforcement of policies based on the user, device, role, application type, and threat profile
Performance of NAT, VPN, and SPI
Use of an IPS
Notes: 4.2.2.4 Stateful Firewall Benefits and Limitations
4.2.2.5 Next Generation Firewalls
4.2.2.6 Video Tutorial - Cisco ASA with FirePOWER Services
4.2.2.7 Activity - Identify the Type of Firewall

## Slide 11: Classic Firewall

## Slide 12: Introducing Classic Firewall
Notes: 4.2.3.1 Introducing Classic Firewall

## Slide 13: Classic Firewall Operation
Notes: 4.2.3.2 Classic Firewall Operation

## Slide 14: Classic Firewall Configuration
Inspection Rules
Choose the internal and external interfaces.
Configure ACLs for each interface.
Define inspection rules.
Apply an inspection rule to an interface.
Notes: 4.2.3.3 Classic Firewall Configuration

## Slide 15: Firewalls in Network Design

## Slide 16: Inside and Outside Networks
Notes: 4.2.4.1 Inside and Outside Networks

## Slide 17: Demilitarized Zones
Notes: 4.2.4.2 Demilitarized Zones

## Slide 18: Zone-Based Policy Firewalls
Notes: 4.2.4.3 Zone-Based Policy Firewalls

## Slide 19: Layered Defense
Considerations for network defense:
Network core security
Perimeter security
Endpoint security
Communications security
Firewall best practices include:
Position firewalls at security boundaries.
It is unwise to rely exclusively on a firewall for security.
Deny all traffic by default. Permit only services that are needed.
Ensure that physical access to the firewall is controlled.
Monitor firewall logs.
Practice change management for firewall configuration changes.
Remember that firewalls primarily protect from technical attacks originating from the outside.
Notes: 4.2.4.4 Layered Defense

## Slide 20: Zone-Based Policy Firewalls
Upon completion of this section, you should be able to:
Explain how Zone-Based Policy Firewalls are used to help secure a network.
Explain the operation of a Zone-Based Policy Firewall.
Configure a Zone-Based Policy Firewall with CLI.

## Slide 21: Zone-Based Policy Firewall Overview

## Slide 22: Benefits of ZPF
Not dependent on ACLs
Router security posture is to block unless explicitly allowed
Policies are easy to read and troubleshoot with C3PL
One policy affects any given traffic, instead of needing multiple ACLs and inspection actions
Notes: 4.3.1.1 Benefits of ZPF

## Slide 23: ZPF Design
Common designs include:
LAN-to-Internet
Firewalls between public servers
Redundant firewalls
Complex firewalls
Design steps:
Determine the zones
Establish policies between zones
Design the physical infrastructure
Identify subsets within zones and merge traffic requirements
Notes: 4.3.1.2 ZPF Design
4.3.1.3 Activity - Compare Classic Firewall and ZPF Operation

## Slide 24: ZPF Operation

## Slide 25: ZPF Actions
Inspect - Configures Cisco IOS stateful packet inspections.
Drop - Analogous to a deny statement in an ACL. A log option is available to log the rejected packets.
Pass - Analogous to a permit statement in an ACL. The pass action does not track the state of connections or sessions within the traffic.
Notes: 4.3.2.1 ZPF Actions

## Slide 26: Rules for Transit Traffic
Rules for Traffic to the Self Zone
Notes: 4.3.2.2 Rules for Transit Traffic
4.3.2.3 Rules for Traffic to the Self Zone
4.3.2.4 Activity - Rules for Transit Traffic

## Slide 27: Configuring a ZPF

## Slide 28: Configure ZPF
Notes: 4.3.3.1 Configure ZPF

## Slide 29: Step 1: Create Zones
Notes: 4.3.3.2 Create Zones

## Slide 30: Step 2: Identify Traffic
Command Syntax for class-map
Sub-Configuration Command Syntax for class-map
Notes: 4.3.3.3 Identify Traffic

## Slide 31: Step 2: Identify Traffic (Cont.)
Example class-map Configuration
Notes: 4.3.3.3 Identify Traffic

## Slide 32: Step 3: Define an Action
Example policy-map Configuration
Command Syntax for policy-map
Notes: 4.3.3.4 Define an Action

## Slide 33: Step 4: Identify a Zone-Pair and Match to a Policy
Example service-policy Configuration
Command Syntax for zone-pair and service-policy
Notes: 4.3.3.5 Identify a Zone-Pair and Match to a Policy

## Slide 34: Step 5: Assign Zones to Interfaces
Notes: 4.3.3.6 Assign Zones to Interfaces

## Slide 35: Verify a ZPF Configuration
Verification commands:
show run | begin class-map
show policy-map type inspect zone-pair sessions
show class-map type inspect
show zone security
show zone-pair security
show policy-map type inspect
ZPF Configuration Considerations
No filtering is applied for intra-zone traffic
Only one zone is allowed per interface.
No Classic Firewall and ZPF configuration on same interface.
If only one zone member is assigned, all traffic is dropped.
Only explicitly allowed traffic is forwarded between zones.
Traffic to the self zone is not filtered.
Notes: 4.3.3.7 Verify a ZPF Configuration
Syntax Checker - Configure Zone-Based Policy Firewall with CLI
4.3.3.8 ZPF Configuration Considerations
4.3.3.9 Video Demonstration - ZPFs

## Slide 36
DÚVIDAS ?!